## Slide 1: Chapter 6 Fundamentals of Digital Video
“Computers and Creativity”
Richard D. Webster, COSC 109 Instructor
Office: 7800 York Road, Room 422 | Phone: (410) 704-2424
e-mail: webster@towson.edu
109 website: https://tigerweb.towson.edu/webster/109/index.html

## Slide 2: Video
motion
a sequence of pictures
frames

## Slide 3: Frame Rate
How fast the pictures are captured
How fast the frames are played back is determined by
Frames per second (fps)

## Slide 4: Broadcast Standards
Digital video resolution
Color spaces
Frame rate
Influenced by analog TV broadcast standards

## Slide 5: Standards for Analog Color TV
NTSC:
  designated by U.S.'s National Television Systems Committee
  U.S., Japan, Taiwan, parts of the Carribean, South America
PAL:
  Phase Alternating Line
  Australia, New Zealand, Western Europe, Asian
SECAM:
  Séquentiel Couleur avec Mémoire
  France, former Soviet Union, Eastern Europe

## Slide 6: Frame Rates of Different Broadcast Standards
Video Type | Frame Rate (frames per second)
NTSC (black-and-white) | 30
NTSC (color) | 29.97
PAL | 25
SECAM | 25
Motion-picture film | 24

## Slide 7: How CRT Monitors and TVs Display Pictures
Picture displayed on CRT is made up of horizontal lines
  NTSC: 525 lines (about 480 lines are picture)
  PAL and SECAM: 625 lines (about 576 lines are picture)
Lines are traced across the screen
  one line at a time
  from top to bottom

## Slide 8: Ways of Tracing Lines From Top to Bottom
Progressive scan:
  from top to bottom in one pass
Interlaced scan:
  in two passes:
    even-numbered lines
    odd-numbered lines

## Slide 9: Interlace Artifacts
Not discernible during normal playback of most videos
DeInterlace
  To remove the interlace artifact
  Common method:
    discard one field
    fill in the gaps by duplicating or interpolating the other field

## Slide 10: Sampling and Quantization of Motion
Temporal:
  sampling rate:
    how frequent you take a snapshot of the motion
    frame rate
    higher sampling rate: higher frame rate
    higher frame rate  more frames for the same duration  larger file size

## Slide 11: Sampling and Quantization of Motion
Each snapshot: a frame
  an image
  digitized based on the same concepts of sampling and quantization of images
Frame Size
  Resolution of the frame image
  Measured in pixel dimensions
  No ppi setting: Unlike digital images, there is no pixel per inch (ppi) setting for video because video is not intended for print but for on screen display.

## Slide 12: Frame Size Examples
 |  | Frame size
NTSC | standard definition | 720 x 480 pixels
 | high definition HDV format | 1280 x 720 pixels 1440 x 1080 pixels
PAL | standard definition | 720 x 576 pixels
Note that the frame size of a video refers to the video’s Resolution.

## Slide 13: Frame Aspect Ratio
the ratio of a frame's viewing width to height
NOT equivalent to ratio of the frame’s pixel width to height.

## Slide 14: Frame Aspect Ratio Examples
4:3
16:9
Example:
Standard definition NTSC standard format
Examples:
Standard definition NTSC wide-screen format
High definition digital video
High definition TV

## Slide 15: Distortion
Pixel Apect Ratios | Distortion
video frame's = display system's | none
video frame's < display system's | stretched horizontally
video frame's > display system's | stretched vertically

## Slide 16: Digital Video Standards
Standard definition
High definition
Digital Television

## Slide 17: The Term DV
Common simple abbreviation for digital video
DV compression and DV format: specific types of digital video compression and format respectively
In this textbook
  DV refers to the specific types of digital video
  DV is NOT used to abbreviate digital video

## Slide 18: Standard Definition DV25 Format
Pixel Dimensions |  | 720  480 (NTSC) | 
Frame Aspect Ratio |  | 4:3 | 16:9
Pixel Aspect Ratio |  | 0.9 | 1.2
Data Rate | Total (video + audio + control information): | 3.6 megabytes per second (MB/s), i.e. about 4.6 minutes of video per gigabyte of storage space | 
 | Video data only: | 25 megabits per second (Mbps); compressed at a fixed rate of 5 :1 | 
Color Sampling Method |  | YUV 4:1:1 | 
Audio Setting | Sampling rate and bit depth: | Two options: 48 kHz, 16-bit 32 kHz, 12-bit | 
widescreen format

## Slide 19: High Definition
Common high definition video formats:
  HDV
  DVCPro HD
  AVCHD
  AVC-Intra
Different video cameras support different high def. format
The name of the supported format is printed on the body of the video camera

## Slide 20: Picture Format Notation
1080
/
60
i
frame height
frame/field frequency
"i": interlaced
"p": progressive

## Slide 21: Frame Size (Resolution) Comparison between Standard Definition and High Definition
By viewing frame size

## Slide 22: Digital Television (DTV)
Signals of DTV are broadcast and transmitted digitally
Need a digital TV set to watch
Standard definition
  704  480, 16:9 and 4:3, progressive and interlaced
  640  480, 4:3, progressive and interlaced
High definition
  1920  1080, 16:9, progressive and interlaced
  1280  720, 16:9, progressive and interlaced
  MPEG-2

## Slide 23: Common Video File Types
File Type | Acronym For | Originally Created By | File Info & Compression | Platforms
.mov | QuickTime movie | Apple | Also audio-only Can be streamed "Fast start" Common compression methods: H.264, Sorenson Video, Animation | Apple QuickTime player, which is available for Mac and Windows
.avi | Audio Video Interleave | Intel | Common compression methods: Microsoft RLE, Intel Indeo Video | Primarily used on Windows but Apple QuickTime player can play AVI files
.mpg .mpeg | MPEG | Motion Picture Experts Group | For DVD-video High definition HDV | Cross-platform
.divx |  | DivX, Inc | Uses DivX codec, which is based on MPEG-4 Popular format for movies because of the high image quality and small file size AVI is a common container file format | May require downloading DivX codec Windows Media Player v11.0 comes with DivX codec

## Slide 24: Common Video File Types
File Type | Acronym For | Originally Created By | File Info & Compression | Platforms
.mp4 | MPEG-4 | Moving Pictures Experts Group | Video codec: H.264 Audio codec: AAC One of the HTML5 video formats | Plays in Web browsers that support the MP4 format of HTML5 video (Safari and IE)
.ogg or .ogv | Audio Video Interleave | Xiph.Org Foundation | Video codec: Theora Audio codec: Vorbis One of the HTML5 video formats Compared to the other two HTML5 video formats, it has lower quality for the same file size | Plays in Web browsers that support the OGG format of HTML5 video (Firefox, Chrome, Opera)
.webm |  | An open source video format from Google | Video codec: VP8 Audio codec: Vorbis One of the HTML5 video formats | Plays in Web browsers that support the WebM format of HTML5 video (Firefox, Chrome, Opera)

## Slide 25: Common Video File Types
File Type | Acronym For | Originally Created By | File Info & Compression | Platforms
.flv | Flash Video | Adobe | Progressive download Can be streamed Common compression methods: H.264, Sorenson Spark, On2 VP6 | Cross-platform Requires Adobe Media Player to play
.f4v | Flash Video | Adobe | Builds on MPEG-4 Part 12 Supports H.264/ACC-based content | A newer Flash Video format than flv Cross-platform Requires Adobe Media Player to play Can be embedded in Flash SWF files
.wmv | Windows Media | Microsoft |  | Requires Windows Media Player to play

## Slide 26: Considerations for File Type
File size restriction
Intended audience
Future editing

## Slide 27: File Size Restriction
For Web:
  high compression
  streaming video
CD-ROM or DVD-ROM playback:
  use data rate that can be handled by your target audience's computer
DVD-video:
  MPEG-2

## Slide 28: Intended audience
Multiple platforms
  cross-platform formats: Apple QuickTime, MPEG, Flash video, Real Video
How your target audience is going to watch your video?

## Slide 29: Future Editing
If the video will be used as a source for future editing:
  Lower compression level
  Choose uncompressed, if
    the frame size is small
    the video duration is extremely short
    you have enough disk space

## Slide 30: General Strategies for Reducing Video Data Rate
Basic ideas:
A video is a sequence of images + audio
Apply strategies for reducing digital image and audio file size.

## Slide 31: General Strategies for Reducing Video File Size
General Strategies for reducing digital image file size
  reduce frame size
  reduce frame rate
  choose a video compressor that allows higher compression
  choose the lower picture quality option
Reduce duration of the video so you have less frames
  not always possible
  will not impact data rate

## Slide 32: Why General Strategies for Reducing Digital Image File Size Work for Video
Reduce frame size because:
  you have less pixels for each frame
Reduce frame rate because:
  you have less frames
Video compression with high compression because:
  some data are discarded
Lower picture quality option because:
  some data are discarded

## Slide 33: Strategies Least Used for Reducing Video Data Rate
Reduce bit depth
  Not all video formats support lower bit depth
  Live videos need 24-bit to look natural
  Some compressors do not support lower bit depth
Reduce sampling rate, bit depth, and channel numbers of the audio
  size of the audio is insignificant compared to that of the picture component in a video

## Slide 34: Compression and Decompression
Compression:
  To reduce file size
  Takes time
  Often takes more time for higher compression
Decompression:
  A compression video file must be decompressed before it is played.
  The decompression method or algorithm depends on how it is originally compressed.
Compression and decompression always go together as a pair.
Codec: compressor/decompressor

## Slide 35: MPEG
Moving Pictures Experts Group Committee who derives standards for encoding video
Allow high compression
MPEG-1, MPEG-2, MPEG-4
What happened to MPEG-3?
  NOT MP3 (which is audio format)
  Intended for HDTV
  HDTV specifications was merged into MPEG-2

## Slide 36: MPEG-1
Video quality comparable to VHS
Originally intended for Web and CD-ROM playback
Frame sizes up to 352  240 pixels
Video format for VCD (VideoCD) before DVD became widespread

## Slide 37: MPEG-2
Supports DVD-video, HDTV, HDV standards
For DVD video production: Export video into DVD MPEG-2 format
For HDV video production: Export video into HDV's MPEG-2 format

## Slide 38: MPEG-4
Newer standard of MPEG family
MPEG-4 targets mobile applications, as in cell phones.